## Slide 1: The Ultimate Blinkin Light
Introduction to Arduino Programming, ESP Boards, and Neo Pixels

## Slide 2: Marcel Chabot
Software Development Lead
Maker
Not a teacher
I’m a total geek and I’m proud of it

## Slide 3: First online Programming Class
Yes, you are guinea pigs.
Please let me know if things are going too fast/slow.
Greatly appreciate your feed back at the end of class.

## Slide 4: Class Outline
Arduino Installation
Hardware Overview
Circuit Building
Code
Debug

## Slide 5: Arduino Installation
Download
  https://www.arduino.cc/en/Main/Software
  Microsoft Store
Install
Add Boards
Add Libraries

## Slide 6: Arduino IDE
Used to write the code for the Arduino/ESP hardware
Global Variables go on top
Setup function happens once
Loop happens over and over again
Lower camel case variable names
// is a comment and doesn’t run

## Slide 7: Adding Boards
Open Arduino
Select File > Preferences
Update the Additional Boards Manager URLs
  https://arduino.esp8266.com/stable/package_esp8266com_index.json
Select Tools > Boards > Boards Manager…
Type ESP8266
Click the Install Button

## Slide 8: ESP Node MCU
Covers a large number of devices.
Digital In/Out (DI/DO)
Pulse Width Modulated output (PWM)
Analog Input (10 bit ADC)
RS-232/SPI/ICSP

## Slide 9: Plug in the MCU
Connect to the computer USB port.
Right click on the Start menu and select Device Manager
There should be a device listed under Ports
If not, the drivers may need to be installed from:
https://www.silabs.com/products/development-tools/software/usb-to-uart-bridge-vcp-drivers

## Slide 10: Blinking LED Code
// the setup function runs once when you press reset or power the board
void setup() {
// initialize digital pin LED_BUILTIN as an output.
pinMode(LED_BUILTIN, OUTPUT);
}
// the loop function runs over and over again forever
void loop() {
digitalWrite(LED_BUILTIN, HIGH); // turn the LED on (HIGH is the voltage level)
delay(1000); // wait for a second
digitalWrite(LED_BUILTIN, LOW); // turn the LED off by making the voltage LOW
delay(1000); // wait for a second
}

## Slide 11: Digital Input/output
Acts like little switches, either On or Off
Greater Than 3 volts = On
Less than 1.5 volts = Off
Mind the gap
Provides 40 mA of current sourcing or sinking
Digital Outputs can also output an 8 bit square wave

## Slide 12: Analog Input
1 Analog output channels
10 bit resolution across 5 volts
Bits = Steps, 10 bits = 1024 steps
Resolution represents the smallest change the device can read
5 Volts / 1024 Steps = 0.0049 volts/step

## Slide 13: PWM
Pulse Width Modulation
Runs at a fixed clock rate
Expressed as percent time High
Pins marked with ~
LED?
Motor?
Piezo?

## Slide 14: The Breadboard
The power lines, 2 on each edge, run vertically
The prototyping lines run horizontally
No lines cross the center gap

## Slide 15: NEOPixels
Initially packaged and sold by Adafruit.
One Wire system (I know there are three)
Used to cover a large variety of self addressing LED systems.
WS2811, WS2812, WS2812B, SK6812
Very timing dependent

## Slide 16: Wiring Considerations
VIN is connected to the voltage from the USB Port
Limited current available when run from USB
VIN can be used to power the MCU.
When powering the MCU and the WS2811 string the current is limited by the wiring and the power supply.
When using a power supply or battery add a 1000 µF, 6.3V or higher capacitor between the power leads.
DON’T USE VIN EXTERNALLY AND USB.

## Slide 17: Power to the Pixels
The normal usage: Pixels X 20ma / 1000
  50 x 20ma/1000 = 1Amp minimum
The full power usage: Pixels x 60ma / 1000
  50 x 60ma/1000 = 3 Amps minimum
The MCU can only do about 500ma, so we will need to watch out.

## Slide 18: Wiring up the Lights

## Slide 19: Libraries Make Everything Better
Select Tools > Manage Libraries
Search for FastLED
Install the FastLED library

## Slide 20: Coding our first Blinking Light

## Slide 21: A little more Code
Variables
  Boolean 0, LOW, false, 1, HIGH, true
  Int -32768 to 32767
  Char a character
Declare
Assign
If / Then / Else
While
For

## Slide 22: If / Then / Else
==, !=, >, <, !
&&, ||
Performs a comparison
Results must be True or False
Condition is after the if in ()
The Action is after the condition in {}
Change together with else if
Default condition with an else
if(val == 1) {
digitalWrite(ledPin, LOW);
}
else if (val == 2) {
digitalWrite(ledPin, HIGH);
}
else {
digitalWrite(errorPin, HIGH);
}

## Slide 23: Repetition
Allows you to perform actions repeatedly
Controlled with variables
Always contains a header and a body with { }
You can loop inside a loop!
Loop
While
For

## Slide 24: Loop

## Slide 25: While

## Slide 26: For

## Slide 27: Going BIG

## Slide 28: Sources for Ideas
https://www.tweaking4all.com/hardware/arduino/adruino-led-strip-effects/

## Slide 29: What about Wifi?
IoT Config for WiFi connections
Showing a page
Interacting with the ESP through a web page
Notes: https://github.com/prampec/IotWebConf

## Slide 30: Libraries Too Add
Select Tools > Manage Libraries
Search for IoTWebConfig
Install the IoTWebConfig library

## Slide 31: IotWebConfig
Starts the device as a WiFi AP at 192.168.4.1
Hosts a configuration web page for WiFi connection details
Can be configured to allow additional parameters
Automatically switches to configured WiFi, and fails back to AP Mode
Includes web page hosting resources

## Slide 32: Examples for Today
Config Page
Color Picker
Pattern Picker
Parsing Query Strings

## Slide 33: Important Concepts
Most Patterns are Loops and must happen with the Loop routine.
Web interaction is a one shot and must “message” the loop to do work.
Don’t judge the ESP platform by my HTML.

## Slide 34: Things for Tomorrow
Web Control Via Web Service
Web Control with Ajax interactive pages
Home system integration
  www.ESPHome.io
  www.home-assistant.io
  www.openhab.org
  www.nodered.org

## Slide 35: Thank you!